## Slide 1: Update on the Large GEM prototype @ Uva & mTPC detector for the TDIS Experiment @ JLab
Kondo Gnanvo
EIC Weekly Meeting, March 26, 2018

## Slide 2: 2 sets of support frames for the large GEM prototype
High cost inner frames for GEMs with spacer grids
4 Inner Frames with 300 µm spacers grid for GEM foils
Precision machining of PERMAGLAS by RESARM (Belgium)
  High material and machining cost
Total cost for all 4 frames = 5.5 k$
Expected delivery in two weeks from today
Low cost outer frames without spacer grids
4 Outer Frames for gas window foils without spacers grid
Each frame made of four G10 pieces cut out in local UVa machine shop
  Low cost: all parts for 4 frames from single 36” × 48” G10 plate
Total cost = 92 $ (material) + UVa machine shop labor
All part for already produced and glued in our lab

## Slide 3: Status of the Large GEM Prototype
Set of 3 pieces for 1 frame
Frame with Glued Kapton gas window
Completed: Sand and glue to the gas window foils to the low cost frames
Completed: Mechanical stretcher for EIC GEM prototype @ minimal cost: Modification of existing stretcher for PRad GEMs
Still waiting for high cost frames from RESARM: they are 2 months behind schedule which is usual for them
Upon reception of the RESARM frames, we can start the assembly ⇨ Minimum 4 weeks including preliminary test of the chamber
Modified PPad Stretcher

## Slide 4: mTPC detector for the TDIS Experiment @ JLab

## Slide 5
Tagged DIS Measurement with RTPC and SBS
Low momentum proton recoil / spectator:
Original idea: Radial TPC (RTPC) a la BoNuS
Super Bigbite

## Slide 6
TDIS mTPC Design
Original idea: Radial TPC (rTPC a la BoNuS / BoNuS12
Fully cylindrical GEM chamber 10 / 30 cm inner / outer diameter
Radial (10 cm) drift E-field perpendicular B-field ⇨ very long track
Pros: No material in active volume, 20K$ electronic channels
Cons: very high particle rate (~700 Mhz in the volume), drift time too long ~ 20 µs for track, challenges with Cylindrical Triple GEMs, momentum resolution etc …
Current design: multiple TPCs (mTPCs) configuration
10 GEM readout / 5 drift cathodes each shared by a pair of GEM readouts
Each TPC block is a standard TPC ⇨ drift E-field (5 cm) parallel to B-field ⇨ shorter track and effective reduction of Moller e- background
Pros: Particle rate ~ 70 MHz / GEM layer, shorter track (1 µs), Detector construction less challenging, momentum resolution
Cons: a lot of material in the active TPC volume, need to minimize GEM material, 25K$ electronic channels

## Slide 7
TDIS mTPC GEM mdule Design
Outer field cage
Drift cathode
Double GEMs
Pad readout
Inner field cage